6A350 C SERIES

OPERATING LIMITS

RPM – Maximum Limit					2800

RMP – Idle						750 – 950

Cylinder Head Temperature:

- Max. (Bayonet Thermocouple)				473 K (200(C, 392(F)

- Max. Continuous at Hottest Cylinder

(Spark Plug Gasket Thermocouple)			523 K (250(C, 482(F)

Oil Temperature:

- Max. Inlet						383 K (110(C, 230(F)

- Min. before Take-Off					313 K ( 40(C, 104(F)

Oil Pressure:

- Operating Range					0.38-0.56 Mpa (3.9-5.7 kG/cm2, 55-80 PSI)

- Idle Range						min. 0.17 Mpa (       1.7 kG/cm2, 8.5 PSI)

Fuel Pressure:

- Carburetor Inlet						min. 0.0034 Mpa (0.035 kGcm2, 0.5 PSI)

max 0.0590 Mpa (0.600 kG/cm2, 8.5 PSI)

Carburetor Inlet Air  Temperature:

- Maximum						323 K (50(C, 122(F)

- Minimum						278 K  ( 5(C,  41(F)

NOTE:  At a high air humidity it is recommended to maintain carburetor inlet air temperature within 283-313 (10-40(C. 50-104(F)

ENGINE & ACCESSORIES WEIGHT

- Weight (Dry Engine)					150 kg/330 lbs

Includes:

- Engine							135 kg/297lbs

- Marvel Schebler Carburetor (MA-5; 10-4865)		2.2 kg/4.84 lbs

- Bendix Magneto (S6RN-21; 10-51365-54)			5.4 kg/11.88 lbs

- SLICK Magneto (6399)					4.6 kg/10.12 lbs

- Ignition Harness					2.7 kg/5.94 lbs

- Spark Plugs (RHB-32E)					1.5 kg/3.3 lbs

- Alternator Drive					1.8 kg/3.96 lbs

- Fuel Pump Drive					1.35 kg/2.97 lbs

Accessories Weight:

- Alternator Prestolite ALX 8421 12			5.5 kg/12.1 lbs

- Starter Prestolite MCL 6502 CWD, 12V			8.7 kg/19.14 lbs

- Fuel Pump A.C. Spark Plug Div.	(4886)			0.45 kg/.99 lbs

- Propeller Pitch Governor Woodward			1.6 kg/3.52 lbs

# Text boxes

New Aviation, Inc.

# 11901 Swearingen, Ste. 54

Austin, Texas  78758-2253

512/837-0593 phone

512/837-7753  fax